2011/00812/FUL	Received on 17 August 2011

Coastal Oil and Gas Limited, 9, Bridgend Business Centre, Bridgend Industrial Estate, Bridgend, CF31 3SH

Coastal Oil and Gas Limited, 9, Bridgend Business Centre, Bridgend Industrial Estate, Bridgend, CF31 3SH

Unit 1, Llandow Industrial Estate, Llandow

Drill and test the insitu lower limestone and associated strata for the presence of gas

SITE AND CONTEXT

The application relates to a site of just under 0.2 ha within the Vale Business Park (Llandow Industrial Estate).  The site is an open area of level concrete hardstanding, probably originating in the wartime use of the site as an airfield.  The site is surrounded by industrial units, many of which are vacant.

DESCRIPTION OF DEVELOPMENT

This planning application is a revised version of a previous submission (ref: 2011/00115/FUL) which was withdrawn on 12 April 2011 due to the discovery of a dwelling house within the Llandow Business Park which had not been taken into account in the submitted noise assessment.  Further noise assessment work has since been carried out to address this omission, and additional information on proposed traffic movements has also been included as part of this submission.

This is a full application for the drilling of a single 160 mm diameter borehole to investigate potential gas resources that may exist in the Carboniferous Lower Limestone Shales and Upper Devonian measures.

The application is made by Coastal Oil and Gas Limited for the purpose (as defined in their submissions) of “drilling to take core samples of Limestone shales with a view to future possible capture and supply of shale gas (unconventional gas) as a clean energy supply and also to penetrate the Upper Devonian measures to test for the presence of conventional gas”.

The drilling is estimated to be to a depth of approximately 650m, and forms part of a continuing program of sampling across South Wales, permissions having previously been granted in Bridgend County Borough Council and Neath Port Talbot County Borough Council.  The applicant advises that further applications are pending in both these areas and one is due to be submitted to Rhondda Cynon Taf Council.

In supporting information, the applicants advise that shale gas (natural gas produced from shale) is becoming an increasingly important source of gas in North America and potential resources exist in many other parts of the world.

This application does not propose hydraulic fracturing, often known as ’fracking’, but rather relates to exploration to see if there is any potential for such viable exploration at the site in future.

The applicants hold a 50% share in a Petroleum Exploration and Development Licence covering the western Vale of Glamorgan granted under the Petroleum Act 1998 by the former Secretary of State for Business, Enterprise and Regulatory Reform in July 2008.  Whilst exploratory boreholes such as this are normally permitted development under Part 22 of the Town & Country Planning (General Permitted Development) Order 1995 (as amended), that Part specifically excludes boreholes for petroleum exploration, including hydrocarbon gases, so that planning permission is required for this proposal.

The submissions indicate that the drilling operation as a whole will take up to 10 weeks, this being sub-divided into the following stages:

- Site Establishment (up to) 1 week;

- Drilling (up to) 5;

- Testing (up to) 2;

- Borehole Restoration (up to) 1; and

- Site Clearance (up to) 1.

The hours of work during the site establishment and site clearance period will be 10 hours per day 08.00 hrs until 18.00 hrs excluding Sunday, with the drilling, testing and restoration period being 24 hour, seven days per week.

Manufacturer’s specifications for the proposed drilling rig (DCR 18 Conrad Combi 500 HD) have been submitted.  The drill rig would be a standard lorry size or track mounted and carried on a trailer.  The rig would be transported to the site very early in the morning when traffic is limited.  Ancillary equipment, including tanks and mess cabins, will be delivered similarly.

On completion all machinery and buildings will be removed and the hole will be plugged with concrete prior to restoration of the surface to a state similar to the existing concrete slab.

To assist Members consideration, the applicant’s supporting statement is provided at Appendix A.

PLANNING HISTORY

There is an extensive planning history on the industrial estate, but the only application of relevance relates to the following:

2011/00115/FUL : Unit 1, Llandow Industrial Estate, Cowbridge.  Drill and test the insitu lower limestone shale and associated strata.  Withdrawn 12 April 2011.

CONSULTATIONS

Llandow Community Council objects due to the inherent risks associated with drilling and testing, and request the Council take the precautionary approach and refuse on the grounds of potential pollution to important water resources.

Colwinston Community Council has responded as follows:

“Colwinston Community Council wishes to record its opposition to the above proposed exploratory shale gas drilling application.  World-wide evidence indicates that even exploratory exercises are extremely noisy and, in view of their 24/7 nature, invasive and disruptive, and because of the geological nature of the underlying rock strata, there is also the probability that a much wider area, even wider than that of the drill site, will be affected by the transmission of noise and seepage of pollutants associated with the process.  The environmental risks are therefore, in the view of this Community Council, unacceptable and the application should therefore be refused.

However, in the event that approval is considered appropriate, it should be conditional on the provision of adequate Public Liability Insurance.  In terms of the exploration exercise the evidence of such projects elsewhere suggests that a minimum un-conditional cover of £500 million would be required with up to £2000 million for any extraction programme.

Colwinston Community Council also wishes to place on record its objection to the assertion that any objections to a future extraction application and its consequences are unacceptable in the context of this application.  The whole objective of the proposed exploration is to determine the viability of extraction and therefore if the results are commercially positive the results will be used to negate and dismiss the grounds for environmental opposition.  Since the environmental and, not to say the least, resource ownership questions are potentially extreme, these factors also justify refusal of the current application.”

St. Donats Community Council has responded as follows:

“There is great concern regarding potential noise pollution, particularly because of the intended 24-hour operation throughout the duration of the test.  The settlements of Marcross, St. Donats and Monknash are significantly close to the site, and it must be stressed that existing sources of noise from the area are often clearly heard.  It is felt that the additional noise from this drilling process would be intrusive, both to the residents of the area and to the large amount of livestock in the surrounding agricultural land, particularly during the hours of darkness.

We consider that the emphasis on attracting tourists, and on a sustainable 'green' local and national agenda, could only be compromised by the implications of this application in a location which is very close to the Heritage Coast and other notable Conservation Areas and is due to host Wales's great cultural festival, the National Eisteddfod, during 2012.

We are also concerned that this re-submission is, by the applicants own admission, apparently made necessary because a major omission was made on the original application regarding a dwelling house near the site.  This provides us with no confidence as to the ability of the applicants to adequately survey the area and provide environmental assurances.”

Llanmaes Community Council advises that its members are extremely concerned at the effect this exploration work for gas could have on the local environment and urge the Council to reject this application.

Cowbridge with Llanblethian Town Council. Requested that they be officially consulted, and that they are aware of a number of concerns from local residents about the impact this might have on the community of Llanblethian.

Environment Agency Wales has no objection subject to conditions controlling the disposal of foul and surface water, the approval of a working method statement, and the provision of precautionary facilities for the storage of oils, fuels or chemicals.   They also offer advice to the applicant on their requirements to address such matters, as well as informing of the need for their Environment Officer to carry out a pollution prevention visit at the site during any future site preparation and drilling/testing, as well as advice on other permitting regimes.  Their letter is attached in full as Appendix B.

The Council’s Highway Development Team raise no highway objections subject to the applicant adhering to the access arrangements identified within item, 6.6 of their supporting information (namely number of movements and the movement of large vehicles from the south via the A4050, A4226 and B4265 to avoid Llysworney Village).

The Director of Legal, Public Protection and Housing Services (Environmental Health : Pollution) have made a number of representations on the application and response to subsequent information.  The final conclusions are summarised as follows:

“1.	A noise impact assessment with regard to surface plant and drilling operations. We understand drilling is a 24hr, seven day week operation.  In isolation and in combination.

The noise assessment provided ref: 2594/ENS1 alludes to the low background noise levels experienced during the night time period in the vicinity.  Having received technical specifications of the drill rig, he has confirmed he is happy with the submitted noise assessment and offers no objection on noise grounds.  He also confirms this is based upon noise based on plant layout and recently provided drill rig noise and that he is happy that the nearby site users are unlikely to be affected at the given level, concurring with Hunter Acoustics submission in respect of calculating noise impact on nearby office uses.

2.	An agreed vibration impact assessment will be required prior to and during any permitted drilling.  Whilst this is an exploratory borehole it may well be challenged and an assessment agreed with the Local Planning Authority can provide useful information on any impact upon local amenity.  This can be appropriately conditioned.

3.	An agreed scheme will be required on the control of dusts from any surface storage of arisings.

4.	I have checked our known private water supplies database.  There are none within a 4.9km radius.  There may be others we are not aware of however.”

Local Ward Members (Llantwit and Llandow-Ewenny) were also consulted.  To date, Councillor Gwyn John (Llantwit Major Ward) has written in objecting on grounds including the impact on the environment, on health, and tourism.  His correspondence is provided at Appendix F.

Dwr Cymru / Welsh Water. To date no representations have been received.  On the previous application, however, they advised that on the basis that this application is for an exploratory borehole, DCWW has no adverse comments to make.  They did, however, advise that future proposals for gas extraction have the potential for contamination of groundwater, such that any future application should be accompanied by an Environmental Statement considering such matters.  Any representations on the current application will be reported at Committee.

Members should note that both the Environment Agency and Welsh Water were written to on 30 September 2011 at Committee’s request, asking that they confirm their comments and if possible substantiate these further.

Campaign for the Protection of Rural Wales (CPRW) objects on grounds that the process of shale gas exploration and exploitation has the potential to significantly detract from the rural nature and amenity of the vale of Glamorgan.  A copy of their representations are provided at Appendix G.

Health and Safety Executive have responded by advising that the public fears about hydraulic fracturing are unfounded and advising that drilling for oil and gas has been undertaken in the UK since the early 1900s and more than 2000 onshore wells have been drilled.  The email is attached at Appendix K.

REPRESENTATIONS

Given its location within the industrial estate, there are no immediate residential neighbours, although a single house – Six Wells Farmhouse – is located in the industrial estate approximately 250 metres to the north.  The other two closest dwellings to the site are The Grove, over 500 metres to the west and Sheepleys’ Farm, some 500 metres to the north.

In addition to the above residential properties, extensive notifications have been undertaken with all premises within the industrial estate and other nearby residential properties, while notification was also given to those persons who submitted representations on the previous application (approximately 250 individual letters having been sent out as a result of the above).  The application was also advertised by site notice on 22nd August 2010.

In response, at the time of writing in excess of 320 letters of objections have been received to the development, raising objections which can generally be categorised into concerns over:- traffic, noise, ground water pollution, chemical pollution, the potential for this proposal to lead to further drilling / significant objections to the impact of ‘fracking’, potential impact on next year’s Eisteddfod.

A number of these letters are based upon a ‘standard’ text which, for Members information, reads as follows:

“I want to express our concerns regarding the resubmitted application for an exploratory bore hole at the site in Llandow to search for shale gas.  As you will note this application is close to our village and I am concerned about the impact it will have upon our environment and quality of life in the village particularly noise pollution, additional transport through the village, contamination of our local water supply and general impact upon this beautiful area and the many tourists we are currently attracting.  How can you justify the financial and economic support the council is currently offering for the Welsh Eisteddfod, which will be sited at Llandow next year - which will greatly promote our area as a wonderful tourist destination and then accept this planning application?

I am alarmed and very concerned by this planning application.  Whilst I appreciate that this is an application for merely exploration purposes, the concerns I have are for the potentially far-reaching consequences of this research activity for communities across the Vale.  If shale gas were to be found, an application would be much harder to refuse, no matter how Councillors, residents and farmers of the area feel, due to current financial circumstances. So please, help us stop this application now before the beautiful countryside we all enjoy is gone forever.

This is one of the most precious parts of South Wales and it is hard to understand how any company would consider such an activity in such a sensitive area.  It is close to the Heritage Coast and is next to areas of Grade 1 agricultural land, very little of which exists across Wales.”

My main concerns regarding this exploratory application are:

- The noise levels during the proposed 7 weeks.  Not only will the drilling machinery itself create a substantial amount of noise 24 hours a day, but the associated noise levels of movement of the metal rods + equipment associated with the drilling process will be significant and in addition to the data provided.

- The impact on local businesses is already an issue, with several businesses located on the industrial estate noting that they will move premises and away from the area should this application be approved.  The Llandow business park is an essential employer for the Western Vale and allowing the exploration for gas would undermine existing businesses and reinforce low status, prejudicing their future role and potential for inward investment in and for the Vale.

- The impact on residents in the area will be significant too – from constant noise levels, increased traffic in the area, and concern over potential environmental and health concerns regarding escaping gases and water contamination.  A big threat too of course is the substantial drop in house prices, devastating the whole local economy, should shale gas be found.

- Water pollution is a real concern, with several private bore holes in the immediate vicinity – though Welsh Water do not record this in their response to the planning application.

- The presence of gas drilling + mining would also be incompatible with and undermine the investment made by the Vale in securing the National Eisteddfod at Llandow, as a shop window for general economic and tourism investments in the Vale of Glamorgan.

- There will be a detrimental impact on the already anticipated boom in tourism in the Vale of Glamorgan if this exploratory gas mining application is approved, as many investors and visitors alike will turn away from a potential gas mining area.

The use of the land at Llandow for local businesses and recreational purposes is important to the Llandow, Wick, Llantwit Major and Cowbridge communities, to the Vale Authority’s strategy and to Welsh Government policies.  I trust that you will take my strong objections into account.

These objections include letters received from Alun Cairns MP and Jane Hutt AM, copies of these representations being provided at Appendices C and D.  Andrew RT Davies AM, also objects on grounds including the impact on the environment, on health, and tourism (see Appendix H).

In addition, a number of the objections have been received from local businesses in and around the Llandow area, both within the Business Park and from further afield, expressing concern about the impact on their businesses, largely as a result of potential impacts from noise, vibration and additional traffic.

A number of examples of the letters of objection are provided at Appendix E.

A local group called ‘The Vale Says No’ has also provided a copy of a letter sent to the Welsh Government requesting that they call the application in (see Appendix I).  For Members information, since the last Committee a letter has been received from the Welsh Government advising that they do not consider the issues to be of more than local importance and, accordingly, that they do not intend to call the application in for determination by Welsh Ministers. A copy of the WG letter is provided at Appendix J.

REPORT

Planning Policies

The Development Plan for the area comprises the Vale of Glamorgan Adopted Unitary Development Plan 1996-2011, which was formally adopted by the Council on 18 April 2005, and within which the following policies are of relevance:

ENV27 - Design of New Developments

ENV29 - PROTECTION OF ENVIRONMENTAL QUALITY

MIN1 - mineral exploration

Report Update

Members will recall that this application was deferred at the 29th September meeting for Members to undertake a site visit.  In addition, Members resolved that Officers write to Welsh Water, the Environment Agency Wales and Environmental Health, requesting that further confirmation is provided that each consultee has no concerns about possible pollution of underground water.

This report is that which was presented to the last Committee, amended to take into account the late representations.

A response has been received from the Environment Agency (see Appendix K) advising that they have no further comments or advice to offer at this stage, and that they are satisfied that all matters within their environmental remit can be satisfied through the relevant planning measures.

A response has also been received from Welsh Water stating as follows:

“We would have some concern if significant volumes of drilling fluid were lost to the formation as this would provide a potential source of pollution to Dwy Cymru groundwater sources.  With respect to this, we would like to understand the content of the drilling fluid to be used and assurance that loss of drilling fluid to the formation during the drilling process will be monitored and how this will be minimised.

We wish to reaffirm the comments made within our letter of the 22 March 2011, and would appreciate your advice on the next steps in the process. We also request details on how the applicant can alleviate our concerns mentioned above”.

In reply to the Dwr Cymru queries, the applicant was contacted and has responded as follows:

“The drilling of the borehole utilises drilling fluids in a closed loop system that will be closely monitored.  The returns from the borehole flow back over the shaker into the tanks.  As the borehole increases in depth more fluids are required in the loop, the fluid is constantly monitored for specific gravity and viscosity by the drilling crew.

In the case of excessive fluid losses in the borehole, lost circulation prevention material can be added to the fluids, these swell in the water and block the fractures where water is being lost.  The limestone measures will be completely cased with steel to prevent fluid losses or gains from the limestone before drilling into deeper measures.

A viscosifier will be added to the drilling fluids to increase the viscosity, this would typically be “Pure Bore” (available on file).  The increase in the viscosity of the fluid will also reduce the possibility of loss of fluid into the formation.

In essence the drilling through the limestone is no different from drilling a water well to extract ground water for drinking purposes.  The same approved substances are utilised to effect control. Once the entire thickness of the Limestone has been penetrated, the whole of the Limestone measure will be cased off and cemented to surface to ensure no ground water pollution could possibly occur.

To summarise all drilling products used will be approved by both the Environment Agency and the Health and Safety Executive before drilling starts.  This drilling operation is nothing to do with fracing or ground stimulation, similar drilling operations are taking place throughout the country for water extraction on a daily basis”.

This response has been directed to Welsh Water and Members will be advised of their further response at Committee.  Nevertheless, on the basis of the above, it is considered that the potentials impacts of drilling on groundwater would be acceptably managed, while the recommended Condition No. 4 in respect of submission of and compliance with a required method statement would cover the operations at the site.

As detailed above, the Welsh Government’s ‘non-intervention’ letter to a recent call-in request is attached at Appendix J.

Issues

Members will recall that a previous application, ref: 2011/00115/FUL, for the same development was previously withdrawn by the applicants prior to being determined at Committee.

Having regard to the nature of submissions, the local context and the nature of representations received to this application, the main issues to consider relate to the principle of the proposed operations, including the risks of pollution from the works proposed, and any impact on local amenity as a consequence of such operations, with particular regard to noise, vibration, dust, and the impact on the local highway network.

The Hydraulic Fracturing / Fracking Process

Exploitation of proven shale gas resources elsewhere in the world has received mixed publicity, with some developments in the USA allegedly having had detrimental effects on water resources.  Whilst any application for exploitation here would have to be considered very carefully, and would undoubtedly require the submission of extensive environmental information as part of an Environmental Impact Assessment, this should not be confused with the current proposal which involves the drilling of a single borehole to assess the bedrock strata.  No ‘fracturing’ of the rock using high pressure chemicals, as may be needed to extract any gas found, is proposed.  In this respect, the operation currently proposed is very similar to other geological exploration boreholes that have been drilled in the Vale in recent years.

While a large number of representations have raised objection to the knock-on implications of allowing the test drilling, insofar as a successful test may lead to subsequent applications for commercial exploitation in the area, the current application is for test drilling only.  In this respect, while the objections are acknowledged and understood, as are the potential implications of such test drilling leading to further application(s) for commercial exploitation, nevertheless it is considered that there are no justifiable or sustainable grounds for objection to the current proposal on the basis that it may lead to such future development.  In this regard it is again emphasised that the impacts of any future proposal can only be made at that time.

Principle of Drilling

Policy MIN1 of the Unitary Development Plan supports mineral exploration works unless there would be an unacceptable impact on landscape character, visual amenity, nature conservation, residential amenity, the Glamorgan Heritage Coast, surface water and ground water resources or scheduled ancient monuments and historic landscapes.  The only criteria relevant to this case are residential amenity and water resources, although these are broadened to consideration of matters relating to noise/ vibration, traffic and potential impacts on the local area in general.  Individual impacts are addressed below.

The supporting text to Policy MIN1 also makes clear that the grant of planning permission for exploratory work will not indicate a presumption in favour of future exploitation.

Visual Impact

The site forms part of a wider industrial site and is largely surrounded by other buildings.  The site is also in a relatively poor condition at present, being used for little other than storage of lorries etc.  In this context, the temporary siting of the 12m high rig and associated equipment will have minimal impact in local views.  In any respect, the rig and equipment will only be in place for a limited time, such that any impacts are temporary.

Noise Impacts

As detailed above, the revised application has been supported by an updated noise report carried out by Hunter Acoustics, which includes assessment of the impact on the nearest residential property at Six Wells Farmhouse.  In addition, following contact with the agent, further submissions have identified the technical specifications of the proposed drilling rig, as well as given further consideration to the impact on nearby office uses.

The report submitted with the application concludes that “we would not therefore assess noise from the drilling works to be an issue on this site”.

The Council’s EHO initially stated that the noise assessment could not be relied upon since it relied on as yet (at that time) unsupported data for the sound power and or pressure level for the drill rig and other associated plant.  The subsequent technical specifications of the drill rig, however, together with details on generator, compressor and vibrating screens have been assessed, and the EHO has now made it clear that he has no objection to the proposal in terms of any impact of noise on nearby homes or businesses.

In response to local concerns about the impact of local businesses from the drilling noise, Hunter Acoustics have further stated as follows:

“The closest offices are approximately 60m from the drill site – predicted noise levels from the drill (source rating 74dB(A) @ 1m) would be around 48dB(A) outside the office.

Taking a 15dB loss through a partially open window gives 33dB(A) (around NR28).

BS8233 ‘Sound Insulation and Noise Reduction for Buildings’ quotes 40-50dB(A) for offices – we are therefore predicting levels well within office criteria.”

The Council’s EHO concurs with this calculation and similarly raises no objections in this regard.

In conclusion on noise matters, therefore, it is emphasised that the application site is located within an industrial area, with the nearest residential dwellings being some 260m and 500+ metres away, these being generally well-screened by large industrial buildings. In this respect, and having regard to the Council’s Environmental Health Officer’s assessment of the impacts associated with this temporary proposal, it is concluded that although drilling is to take place 24 hours per day, the limited timescale, distance from dwellings and degree of screening are such that any noise impact on residential amenity would be minimal, and transitory at worst.  In addition, any impact from noise associated with the proposal on local businesses would not be so great as to justify withholding consent, especially bearing in mind the temporary (maximum 10 weeks, 5 weeks for drilling) duration of the works.

Vibration

The impact of ground vibration from the operation has also been considered but from extensive experience with drilling in quarries it appears that any ground vibration created by drilling is restricted to a very small area around the rig.

In their submissions, the applicant states that a number of factors will limit the effects on vibration on local residents, including the formation of local bedrock, and the use of rotary drilling methods to minimise vibration.  They also that they will, if required, undertake a vibration monitoring scheme prior to and during the drilling period in accordance with BS 6472-1:2008 and BS 5228-2:2009.  In this regard, the EHO has raised no objections but considers it is appropriate to require a Vibration Impact Assessment (before and during) to inform their analysis of impacts at the site in the expectation that complaints may be received.

Dust

The EHO has raised no objection subject to an appropriate condition requiring an agreed scheme on the control of dusts from any surface storage of arisings.

Water Resources

Issues of water resource protection from a single exploratory borehole are also likely to be limited.  The submissions indicate that the control of ground water during the drilling of this well will by the density of the drilling fluids which would prevent any major water ingress.  The main aquifer has been identified in the Carboniferous Limestone and this will be completely sealed with steel casing cemented into place, which they advise is a recognised method of sealing an aquifer by the Environment Agency.

In this regard, the Environment Agency has raised no objection subject to the imposition of appropriate conditions to prevent pollution and the EHO has advised that their known private water supplies database shows none within a 4.9km radius.  There may be others they are not aware of however.

The schemes required by the EAW conditions will need to be approved and implemented on site before any drilling takes place.

Impact on Highway Safety / Transport Network

Given the relatively low level of traffic associated with the proposal, there would be no adverse impact on the highway network as a result of the use itself.  The highway officer has raised no objections to the development, but considers that the use should be conditioned to accord with the supporting information about movements which is primarily related to the movement of HGVs from the south via the A4050, A4226 and B4265 to avoid Llysworney Village.  An appropriate condition is therefore recommended to that effect.

Similar Test Drilling Approvals

Members should be aware that Bridgend CBC has approved at least two similar exploratory boreholes, these being on the former St. Johns Colliery site (Bridgend reference P/06/999/FUL and P/06/999/FUL).

Other Matters

A number of local residents have raised concerns about the impact on the Eisteddfod planned for Llandow next year.  The impacts as described above, however, are considered to be minor in nature and to have no material impact on such an event, even if they were to be conducted at the same time.  Should Members consider such concerns to be of overriding importance, then a condition could be recommended requiring that the drilling operations are not undertaken during the 2012 Eisteddfod (between 4th and 11th August 2012).

Concluding Comments

In conclusion, it is noted that there have been a substantial number of objections to the proposal, both in terms of the physical impacts of the drilling itself and to the potential impacts associated with any future commercial exploitation as a direct result of the test drilling.  Nevertheless, while these views are wholly acknowledged, and the extent of concern about the test drilling itself and any future exploitation as a consequence, a factual analysis of the proposals leads to the conclusion that, whilst the potential environmental impacts of gas exploitation would require very careful consideration of any subsequent planning application, there are no reasonable or sustainable grounds on which to refuse this specific small-scale, temporary, proposal for a single exploratory borehole subject to the precautionary conditions to control environmental impacts as outlined in the recommended conditions below.

CONCLUSION

The decision to recommend that planning permission be granted has been taken in accordance with Section 38 of The Planning and Compulsory Purchase Act 2004, which requires that, in determining a planning application the determination must be in accordance with the Development Plan unless material considerations indicate otherwise.  The Development Plan comprises the Vale of Glamorgan Adopted Unitary Development Plan 1996-2011.

Having regard to the provisions of Policies MIN 1, ENV27 and ENV29 of the adopted Unitary Development Plan it is concluded that the proposal meets the objectives of those policies in respect of amenity, protection of ground and surface water resources and the character and appearance of the local area.

RECOMMENDATION

APPROVE subject to the following condition(s):

1.	The development hereby permitted shall be begun before the expiration of five years from the date of this permission.

Reason:

To comply with the requirements of Section 91 of the Town and Country Planning Act 1990.

2.	No operations authorised by this permission, with the exception of the site restoration works set out in Section 7.10 of the supporting statement submitted with the application, shall take place after a period of eight weeks following the commencement of drilling operations on the site.

Reason:

In the interests of amenity and to meet the objectives of Policy MIN 1 of the adopted Unitary Development Plan.

3.	The drilling rig to be used in the drilling operations hereby approved shall be a DCR 18 Conrad Combi 500 HD (with a typical noise level at 1 metre not exceeding 74 dBa) in accordance with the submitted equipment profile and specification, unless otherwise approved in writing by the local planning authority.

Reason:

In order to protect local amenity in accordance with Policy ENV29 of the adopted Unitary development Plan, since the impact on nearby properties has only been assessed by the submitted noise assessment on the basis of  a 74dBa noise level at 1m as identified on the manufacturers equipment profile and specification.

4.	Notwithstanding the submitted documents, prior to any drilling taking place on the site a detailed working method statement shall be submitted in writing to and approved by the Local Planning Authority, and all operations shall thereafter be carried out in accordance with the approved details.

Reason:

Since the construction phase of any proposed development poses significant risks to controlled waters, specifically diffuse pollution to the water environment arising from ground works, and in the interests of amenity and to meet the objectives of Policies MIN 1 and ENV27 of the adopted Unitary Development Plan.

5.	Drilling shall not commence until such time as a Vibration Impact Assessment – covering monitoring prior to and during the drilling period in accordance with BS 6472-1:2008 and BS 5228-2:2009 - has been submitted to and agreed in writing by the local planning authority, and the development shall thereafter be monitored in accordance with such agreed scheme.

Reason:

To inform the Council’s analysis of any impacts at the site from vibration caused as a result o the drilling hereby approved, and to comply with Policy ENV29 of the Adopted Unitary Development Plan.

6.	Any facilities for the storage of oils, fuels and chemicals shall be sited on impervious bases and surrounded by impervious bund walls.  The size of the bunded compound shall be at least equivalent to the capacity of the tank plus 10%.  If there is a multiple tankage, the compound should be at least equivalent to the capacity of the largest tank plus 10%.  All filling points, vents and sight glasses must be located within the bund.  There must be no drain through the bund floor or walls.

Reason:

To prevent pollution of the water environment, and to ensure compliance with the terms of Policy ENV27 of the Unitary Development Plan.

7.	Full details of a scheme for the disposal of foul and surface water drainage shall be submitted to and approved in writing by the Local Planning Authority and the approved scheme shall be fully implemented in accordance with the approved details prior to any drilling operations or site preparation taking place on the site. The approved scheme shall include proposals for the treatment and disposal of suspended solids from surface water run-off and shall include emergency procedures to be implemented where any failure results in the pollution of controlled waters.

Reason:

To mitigate the risks of pollution and to ensure compliance with the terms of Policy ENV27 of the Unitary Development Plan.

8.	Within three months of the completion of drilling operations all plant, machinery and buildings shall be removed from the site and the site shall be restored in accordance with the details set out in Section 7.10 of the statement accompanying the application or any alternative scheme that may first be agreed in writing by the Local Planning Authority.

Reason:

In the interests of amenity and  to meet the objectives of Policies MIN 1 and ENV27 of the adopted Unitary Development Plan.

9.	Prior to any drilling operations taking place, a scheme for the treatment, storage and disposal of any dust created by the operation shall be submitted in writing to and approved by the Local Planning Authority and the approved scheme shall thereafter be retained in operation throughout any periods of drilling on the site.

Reason:

In the interests of amenity and to meet the objectives of Policies MIN 1 and ENV27 of the adopted Unitary Development Plan.

10.	Vehicular access to the site shall only be made in accordance with section 6.6 of the supporting information and, in particular heavy traffic (such as the rig, drill pipe and cabins) shall approach and leave the site only from / to the south via the A4050, A4226 and B4265 to avoid Llysworney Village.

Reason:

In the interests of highway safety an to ensure compliance with Policy ENV27 of the Adopted Unitary Development Plan.

NOTE:

Please note that this consent is specific to the plans and particulars approved as part of the application.  Any departure from the approved plans will constitute unauthorised development and may be liable to enforcement action.  You (or any subsequent developer) should advise the Council of any actual or proposed variations from the approved plans immediately so that you can be advised how to best resolve the matter.

In addition, any conditions that the Council has imposed on this consent will be listed above and should be read carefully.  It is your (or any subsequent developers) responsibility to ensure that the terms of all conditions are met in full at the appropriate time (as outlined in the specific condition).

The commencement of development without firstly meeting in full the terms of any conditions that require the submission of details prior to the commencement of development will constitute unauthorised development.  This will necessitate the submission of a further application to retain the unauthorised development and may render you liable to formal enforcement action.

Failure on the part of the developer to observe the requirements of any other conditions could result in the Council pursuing formal enforcement action in the form of a Breach of Condition Notice.