Vale of Glamorgan County Council

Dock Office

Holton Road

Barry Docks

Barry

CF63 4RT

|  | Date: 07/07/2016 |
| --- | --- |
|  | Our Ref: PLA0020967 |
|  | Your Ref: 2015/00843/FUL |

# Dear Sir

Grid Ref: ST1626067726 316260 167726

Site:   Sully Sports & Social Club South Road

Development: Development of sports & social club, inc demolition of existing club house & construction of new, caravan site & building, proposals for up to 200 dwellings.

We refer to your planning consultation relating to the above site, and we can provide the following comments in respect to the proposed development.

We would request that if you are minded to grant Planning Consent for the above development that the    Conditions and Advisory Notes provided below are included within the consent to ensure no detriment to existing residents or the environment and to Dwr Cymru Welsh Water's assets.

SEWERAGE

Conditions

No building shall be occupied until a point of connection on the public sewerage system as has been identified by a hydraulic modelling assessment, which shall be first submitted to and approved by the local planning authority. Thereafter the connection shall be made in accordance with the recommended connection option following the implementation of any necessary improvements to the sewerage system, as may be identified by the hydraulic modelling assessment.

Reason: To prevent hydraulic overloading of the public sewerage system, to protect the health and safety of existing residents and ensure no pollution of or detriment to the environment.  No building shall be occupied until the drainage system for the site has been completed in accordance with the approved details.

Thereafter no further surface water and/or land drainage shall be allowed to connect directly or indirectly with the public sewerage system.

Reason: To prevent hydraulic overloading of the public sewerage system, to protect the health and safety of existing residents and ensure no pollution of or detriment to the environment

The proposed development site is crossed by a public sewer with the approximate position being marked on the attached Statutory Public Sewer Record.  The position shall be accurately located marked out on site before works commence and no operational development shall be carried out within 3 metres either side of the centreline of the public sewer.

Reason: To protect the integrity of the public (sewer/sewers) and avoid damage thereto protect the health and safety of existing residents and ensure no pollution of or detriment to the environment

Advisory Notes

The applicant may need to apply to Dwr Cymru / Welsh Water for any connection to the public sewer under S106 of the Water industry Act 1991. If the connection to the public sewer network is either via a lateral drain (i.e. a drain which extends beyond the connecting property boundary) or via a new sewer (i.e. serves more than one property), it is now a mandatory requirement to first enter into a Section 104 Adoption Agreement (Water Industry Act 1991). The design of the sewers and lateral drains must also conform to the Welsh Ministers Standards for Gravity Foul Sewers and Lateral Drains, and conform with the publication "Sewers for Adoption"- 7th Edition. Further information can be obtained via the Developer Services pages of www.dwrcymru.com

The applicant is also advised that some public sewers and lateral drains may not be recorded on our maps of public sewers because they were originally privately owned and were transferred into public ownership by nature of the Water Industry (Schemes for Adoption of Private Sewers) Regulations 2011.  The presence of such assets may affect the proposal.  In order to assist us in dealing with the proposal the applicant may contact Dwr Cymru Welsh Water on 0800 085 3968 to establish the location and status of the apparatus. Under the Water Industry Act 1991 Dwr Cymru Welsh Water has rights of access to its apparatus at all times.

SEWAGE TREATMENT

No problems are envisaged with the Waste Water Treatment Works for the treatment of domestic discharges from this site.

WATER SUPPLY

Before construction works commence on site, a hydraulic modelling assessment shall be undertaken by the developer in liaison with Dwr Cmyru Welsh Water, in order to assess the effect the proposed development will have on the existing water supply network, together with any necessary associated infrastructure works.

Reason: To protect the integrity of the existing water supply system

There shall be no beneficial use or occupation of any of the buildings hereby approved until such time that any necessary water infrastructure works required by the hydraulic modelling assessment referred to in the above condition have been completed and approved by Dwr Cymru Welsh Water and the Local Planning Authority has been informed in writing of its completion.

Reason: To ensure that the proposed development does not adversely affect the integrity of the existing water supply system.

Our response is based on the information provided by your application.  Should the proposal alter during the course of the application process we kindly request that we are re-consulted and reserve the right to make new representation.

If you have any queries please contact the undersigned on 0800 917 2652 or via email at developer.services@dwrcymru.com

Please quote our reference number in all communications and correspondence.

# Yours faithfully,

Clare Powell

Development Control Officer

Developer Services