# Vale of Glamorgan

Highway Authority Observation Sheet

| Planning Application Ref: | 2017/00724/RES |
| --- | --- |
| Observations By: | Mr Lee M Howells |
| Date: | 22 November 2017 |
| Location: | Land at Caerleon Road, Dinas Powys |
| Proposal: | Approval of all reserved matters on outline consent 2014/00282/OUT for residential development |
| Case Officer: | Mrs. Y. J. Prichard |

No highway Objections would be raised to the proposals in principle subject to the following conditions being satisfied in the interest of highway safety / public safety and the free flow of traffic along the highway network:-

- Notwithstanding the submitted Proposed Site Plan, reference 5567/P/10 Rev T and 	associated engineering drawings  no works whatsoever shall commence on the 	development until full Engineering details and associated calculations where applicable of 	the proposed access / internal road arrangement have been submitted incorporating vision	splays, Street lighting, road signs, street lighting, surface water drainage strategy and any 	retaining structures retaining or adjacent to the highway / public open space have been 	submitted to and duly certified by a Professional Engineer.																				Reason :-	In the interest of highway / Public Safety.

- The developer will be required to enter into a legally binding agreement to secure the		proper implementation of the proposed highway works, connections with the existing		highway network and associated works which shall incorporate the appropriate bond.																Reason :-	To ensure the minimum Design and Construction Standards are 					achieved in the interests of Highway / Public Safety.

- The proposed works shall incorporate resurfacing of a section of the Caerleon Road 	fronting the proposed site access works extending for full site frontage of the site up to 	and inclusive of the junction with Caerleon Close its connection with and ( carriageway 	and footways  and the provision of uncontrolled pedestrian crossing facilities 																	Reason :-	To ensure the minimum Design and Construction Standards are achieved				in the interests of Highway / Public Safety.

Continued overleaf

- The proposed vehicular access onto Caerleon Road shall incorporate and maintain 	thereafter a minimum vision splay of site frontage 43m x 3m in both direction along the	adopted highway as identified within drawing 5567/P/10 Rev T.																		Reason :-	In the interest of highway / Public Safety.

- All proposed vehicular access / junction shall be constructed at right angles to the 	adjoining road																										Reason :-	In the interests of highway safety

- Unless otherwise agreed with the Local Planning Authority the gradient of any			proposed vehicular access / driveways serving the individual plots shall not exceed		5 % ( 1:20 for the first 6m and thereafter shall not be steeper than 12.5% ( 1 in 8 ).																Reason :-	To ensure design standards are achieved in the interests of highway /			public safety.

- No boundary walls ( inclusive of piers ), fencing, gates or Planting shall be erected or		planting within the area located within the area of land within the ownership / control of	the applicant required to provide and maintain the required vision splays as identified 	within drawing 5567/P/10 Rev T.																								Reason :-	In the interest of highway / Public Safety.

- Not withstanding the submitted Engineering drawings the developer will be required to		incorporate the provision of new Permanent / Temporary Traffic Regulatory Orders 		( TRO’s ) as deemed necessary by the Local Planning Authority to achieve the required	speed limits, and to manage on road parking.																						Reason :-	In the interest of highway / Public Safety and the free flow of traffic along				the adopted highway network.

- The Highway Authority will require at the developers expense to carry out prior to 		commencing any works a Condition Survey along agreed haulage route the extent to be	agreed with The Councils Highway Network Manager which shall undertaken by a 		suitably qualified and experienced an independent Highway Maintenance Consultant 		to be approved by the Local Highway / Planning Authority.																				Reason :-	In the interest of highway / Public Safety

Continued overleaf

- The Highway Authority will require at the developers expense a Second Condition 		Survey along agreed haulage route the extent to be agreed with The Councils Highway	Network Manager to be undertaken by the approved independent Highway 	Maintenance Consultant on completion of the last property or such time that the			Highway Authority instruct. 																								Reason :-	In the interest of highway / Public Safety

- The Highway Authority will require at the developers expense to carry out any remedial 	works identified with the second condition survey that the Highway Authority Considers		necessary as direct result of the works.																							Reason :-	In the interest of highway / Public Safety.

- The provision of a Construction Management / haulage route plan together with any 	Proposed Temporary Road Closures and other Temporary or Permanent Traffic 	Regulations required associated with the offsite Highway Improvement Works or the 	internal Roads within the Development to be submitted to and approved by the Local 		Planning Authority prior to commencing any works.																				Reason :-	In the interest of highway / Public Safety and the free flow of traffic along				the adopted highway network.

- No Lorries shall deliver / leave the site during the peak am / pm hours and half hour 		either side of the times school commencing and ending to minimize the congestion to		surrounding highway network and conflicts between site traffic.																			Reason :-	In the interest of highway / Public Safety and the free flow of traffic along 				the adopted highway network.

- Provide and maintain facilities for wheel cleansing shall be provided for the duration		of the works to be approved by the Local Planning Authority prior to any site clearance /	construction works commencing on site. 																						Reason :-	In the interest of highway / Public Safety.

- No materials whatsoever shall to deposited or stored within the limits of the adopted		highway in the interest of highway / Public Safety and the free flow of traffic along the		adopted highway.																										Reason :-	In the interest of highway / Public Safety and the free flow of traffic along				the adopted highway.

Continued overleaf

- Onsite Parking areas shall be surfaced in a bound or block paved material to be		agreed by the Local Planning Authority prior to beneficial occupation.																		Reason :-	To ensure a minimum standard of parking when the development is			brought into use and in the interest of Highway / Public Safety.

- No surface, roof water or other deleterious material from the site shall discharge or		migrate onto the adopted highway. Applicant to make provisions to deal with the		above within the confines of the site. 																						Reason :-	In the interest of highway Safety and environmental management.

Lee M Howells – 22nd November 2017									Principal Engineer

Highway Development

Planning Officer:- Mrs Yvonne Prichard / Mr Steve Butler

Advisory

- Traffic Regulation Orders - A minimum of 12 week’s notice is required to implement a 	Temporary or Permanent Traffic Regulatory Orders should the closure or other order be		agreed requests for any such orders must be submitted in writing to Operational Manager 	Highways & Engineering, Alps Depot Wenvoe, Vale of Glamorgan.