| I / To: | Mr. S. D. Butler |  | Oddi Wrth / From: | D Margetson |
| --- | --- | --- | --- | --- |
| Adran / Dept: | Planning Department |  | Ein cyf / Our ref: | SRS/E/DMM/2017/01203/FUL |
| Dyddiad / Date: | 23/11/2017 |  | Ffôn / Tel: | 03001236696 |
| Eich Cyf / Your Ref: | 2017/01203/FUL |  | Ebost / Email: | dmmargetson@valeofglamorgan.gov.uk |

Subject: Cog Moors Wastewater Treatment Works, Cardiff Road, Dinas Powys;  The change of use of land as an extension to the existing wastewater treatment works site and the construction of an Advanced Anaerobic Digestion (AAD) Plant, together with associated landscaping and mitigation measures and the formation of temporary construction compounds

Planning APPLICation No:  2017/01203/FUL

Further to receipt of the above accepted planning applications, I would like to provide comments

in relation to potential contaminative issues on behalf of SRS: Environment Team:-

The proposal is for construction of an Advanced Anaerobic Digestion (AAD) Plant; including the demolition of and modifications to some existing plant and equipment; together with associated landscaping and mitigation measures and the formation of a temporary construction compound.

Recent and ongoing commercial activities at the development site may have caused the land to become contaminated and therefore may give rise to potential risks to human health and the environment for the proposed end use. The proposed new permanent structures will not normally be occupied. However there are potential risks to human health from contaminants for construction workers and post-development site maintenance workers.

A contamination assessment is requested to identify any such risks and ensure appropriate mitigation/remediation is undertaken.

Should there be any importation of soils to develop the landscaped areas of the development, or any site won recycled material, or materials imported as part of the construction of the development, then it must be demonstrated that they are suitable for the end use. This is to prevent the introduction or recycling of materials containing chemical or other potential contaminants which may give rise to potential risks to human health and the environment for the proposed end use.

Shared Regulatory Services requests the inclusion of the following conditions and informative statements in accordance with CIEH best practice and to ensure that the safety of future occupiers is not prejudiced.

CONDITIONS

PC14A. CONTAMINATED LAND MEASURES – ASSESSMENT

Prior to the commencement of the development an assessment of the nature and extent of contamination shall be submitted to and approved in writing by the Local Planning Authority.  This assessment must be carried out by or under the direction of a suitably qualified competent person * in accordance with BS10175 (2011) Code of Practice for the Investigation of Potentially Contaminated Sites and shall assess any contamination on the site, whether or not it originates on the site.

The report of the findings shall include:

- (i) 	a desk top study to identify all previous uses at the site and potential contaminants associated with those uses and the impacts from those contaminants on land and controlled waters.  The desk study shall establish a ‘conceptual site model’ (CSM) which identifies and assesses all identified potential source, pathway, and receptor linkages;

- (ii)	an intrusive investigation to assess the extent, scale and nature of contamination which may be present, if identified as required by the desk top study;

(iii) 	an assessment of the potential risks to:

- human health,

- groundwaters and surface waters

- adjoining land,

- property (existing or proposed) including buildings, crops, livestock, pets,

woodland and service lines and pipes,

- ecological systems,

- archaeological sites and ancient monuments; and

- any other receptors identified at (i)

- (iv)	an appraisal of remedial options, and justification for the preferred remedial option(s).

All work and submissions carried out for the purposes of this condition must be conducted in accordance with DEFRA and the Environment Agency’s ‘Model procedures for the Management of Land Contamination, CLR 11’ (September 2004) and the WLGA / WAG / EA guidance document ‘ Land Contamination: A guide for Developers’ (2012), unless the Local Planning Authority agrees to any variation.

* A ‘suitably qualified competent person’ would normally be expected to be a chartered member of an appropriate professional body (such as the Institution of Civil Engineers, Geological Society of London, Royal Institution of Chartered Surveyors, Institution of Environmental Management) and also have relevant experience of investigating contaminated sites.

Reason: To ensure that information provided for the assessment of the risks from land contamination to the future users of the land, neighbouring land, controlled waters, property and ecological systems is sufficient to enable a proper assessment.

PC14B. CONTAMINATED LAND MEASURES – REMEDIATION & VERIFICATION PLAN

Prior to the commencement of the development a detailed remediation scheme and verification plan to bring the site to a condition suitable for the intended use by removing any unacceptable risks to human health, controlled waters, buildings, other property and the natural and historical environment shall be submitted to and approved in writing by the Local Planning Authority. The scheme shall include all works to be undertaken, proposed remediation objectives and remediation criteria, a timetable of works and site management procedures. The scheme must ensure that the site will not qualify as contaminated land under Part 2A of the Environmental Protection Act 1990 in relation to the intended use of the land after remediation.

All work and submissions carried out for the purposes of this condition must be conducted in accordance with DEFRA and the Environment Agency’s ‘Model procedures for the Management of Land Contamination, CLR 11’ (September 2004) and the WLGA / WAG / EA guidance document ‘ Land Contamination: A guide for Developers’ (July 2012), unless the Local Planning Authority agrees to any variation.

Reason: To ensure that any unacceptable risks from land contamination to the future users of the land , neighbouring land, controlled waters, property and ecological systems are minimised, and to ensure that the development can be carried out safely without unacceptable risks to workers, neighbours and other offsite receptors.

PC14C. CONTAMINATED LAND MEASURES - REMEDIATION & VERIFICATION

The remediation scheme approved by condition x (PC14B above) must be fully undertaken in accordance with its terms prior to the occupation of any part of the development unless otherwise agreed in writing by the Local Planning Authority. The Local Planning Authority must be given two weeks written notification of commencement of the remediation scheme works.

Within 6 months of the completion of the measures identified in the approved remediation scheme, a verification report that demonstrates the effectiveness of the remediation carried out must be submitted to and approved in writing by the Local Planning Authority.

All work and submissions carried out for the purposes of this condition must be conducted in accordance with DEFRA and the Environment Agency’s ‘Model procedures for the Management of Land Contamination, CLR 11’ (September 2004) and the WLGA / WAG / EA guidance document ‘ Land Contamination: A guide for Developers’ (July 2012), unless the Local Planning Authority agrees to any variation.

Reason : To ensure that any unacceptable risks from land contamination to the future users of the land , neighbouring land, controlled waters, property and ecological systems are minimised, and to ensure that the development can be carried out safely without unacceptable risks to workers, neighbours and other offsite receptors.

PC14D. CONTAMINATED LAND MEASURES – UNFORESEEN CONTAMINATION

In the event that contamination is found at any time when carrying out the approved development that was not previously identified it must be reported in writing within 2 days to the Local Planning Authority, all associated works must stop, and no further development shall take place unless otherwise agreed in writing until a scheme to deal with the contamination found has been approved.  An investigation and risk assessment must be undertaken and where remediation is necessary a remediation scheme and verification plan must be prepared and submitted to and approved in writing by the Local Planning Authority. Following completion of measures identified in the approved remediation scheme a verification report must be submitted to and approved in writing by the Local Planning Authority. The timescale for the above actions shall be agreed with the LPA within 2 weeks of the discovery of any unsuspected contamination.

Reason: To ensure that any unacceptable risks from land contamination to the future users of the land , neighbouring land, controlled waters, property and ecological systems are minimised, and to ensure that the development can be carried out safely without unacceptable risks to workers, neighbours and other offsite receptors.

PC15A IMPORTED SOIL

Any topsoil [natural  or manufactured],or subsoil, to be imported shall be assessed for chemical or other potential contaminants in accordance with a scheme of investigation which shall be submitted to and approved in writing by the Local Planning Authority in advance of its importation. Only material approved by the Local Planning Authority shall be imported. All measures specified in the approved scheme shall be undertaken in accordance with the relevant Code of Practice and Guidance Notes.

Subject to approval of the above, sampling of the material received at the development site to verify that the imported soil is free from contamination shall be undertaken in accordance with a scheme and timescale to be agreed in writing by the LPA.

Reason: To ensure that the safety of future occupiers is not prejudiced.

PC15B IMPORTED AGGREGATES

Any aggregate  (other than virgin quarry stone) or recycled aggregate material to be imported shall be assessed for chemical or other potential contaminants in accordance with a scheme of investigation which shall be submitted to and approved in writing by the Local Planning Authority in advance of its importation. Only material approved by the Local Planning Authority shall be imported. All measures specified in the approved scheme shall be undertaken in accordance with the relevant Code of Practice and Guidance Notes.

Subject to approval of the above, sampling of the material received at the development site to verify that the imported material is free from contamination shall be undertaken in accordance with a scheme and timescale to be agreed in writing by the LPA.

Reason: To ensure that the safety of future occupiers is not prejudiced.

PC15C USE OF SITE WON MATERIALS

Any site won material including soils, aggregates, recycled materials shall be assessed for chemical or other potential contaminants in accordance with a sampling scheme which shall be submitted to and approved in writing by the Local Planning Authority in advance of the reuse of site won materials. Only material which meets site specific target values approved by the Local Planning Authority shall be reused.

Reason: To ensure that the safety of future occupiers is not prejudiced.

ADVISORY/INFORMATIVE

R4 CONTAMINATION AND UNSTABLE LAND ADVISORY NOTICE

The contamination assessments and the affects of unstable land are considered on the basis of the best information available to the Planning Authority and are not necessarily exhaustive.  The Authority takes due diligence when assessing these impacts, however you are minded that the responsibility for

(i) determining the extent and effects of such constraints;

(ii) ensuring that any imported materials (including, topsoils, subsoils, aggregates and recycled or manufactured aggregates/ soils) are chemically suitable for the proposed end use.  Under no circumstances should controlled waste be imported. It is an offence under Section 33 of the Environmental Protection Act 1990 to deposit controlled waste on a site which does not benefit from an appropriate waste management license.  The following must not be imported to a development site;

-    Unprocessed / unsorted demolition wastes.

-    Any materials originating from a site confirmed as being contaminated or

potentially contaminated by chemical or radioactive substances.

- Japanese Knotweed stems, leaves and rhizome infested soils.  In addition to section 33 above, it is also an offence under the Wildlife and Countryside Act 1981 to spread this invasive weed; and

(iii) the safe development and secure occupancy of the site rests with the developer.

Proposals for areas of possible land instability should take due account of the physical and chemical constraints and may include action on land reclamation or other remedial action to enable beneficial use of unstable land.

The Local Planning Authority has determined the application on the basis of the information available to it, but this does not mean that the land can be considered free from contamination.

Deborah Margetson

Specialist Services Officer, Environment

Shared Regulatory Service

Bridgend, Cardiff & the Vale of Glamorgan