| To / I: | Yvonne Pritchard |  | From / Oddi Wrth: | Operational Manager Highways and Engineering |
| --- | --- | --- | --- | --- |
| Dept / Adran: | Planning |  |  |  |
|  |  |  | My Ref / Cyf: | HE/SP/GTD/L5/1 |
| Date / Dyddiad: | 03/08/2018 |  | Tel / Ffôn: | 029 20673277 |
| Your Ref / Eich Cyf: | P/DC/LC/YP/2018/00359/FUL |  | Fax / Ffacs: | 029 20673114 |

Subject / Testyn:	Planning Application No. 2018/00359/FUL Meliden, Sunnycroft Lane, Dinas Powys

Proposal: 	Replacement dwelling on site of former house burned down

This site is not located in DAM zones at risk of tidal or fluvial flooding and NRW maps indicate that there is a very low risk of surface water flooding at the site. However a low risk of surface water flooding does exist to the adjacent highway servicing the property.

The application form submitted does not provide any information with regard to the disposal of surface water drainage of the proposed development. For all new developments, infiltration should be the primary method of surface water disposal, prior to any other method being considered and evidence of on-site infiltration testing should be submitted prior to approval of a surface water drainage system. Therefore, prior to work commencing on site, a full drainage plan demonstrating how roof and yard water will be disposed of shall be submitted to and approved by the LPA. Should infiltration techniques be used, evidence of on-site porosity testing shall also be provided. Soakaways must not be sited within 5m of a building or the highway, and it should be demonstrated that there is adequate space on site for the provision of a soakaway.

No details on the management and maintenance of the proposed drainage system have been included with this application. A management plan which includes details on future management responsibilities for the site and its drainage assets should be submitted and approved in writing by the Local Planning Authority.

Conditions:

Given the above, no development shall commence on site until a detailed scheme for the surface water drainage of the site, showing how road and roof / yard water will be dealt with has been submitted to and approved in writing by the Local Planning Authority. If infiltration techniques are used, then the plan shall include the details of field percolation tests. Any calculation for onsite attenuation or discharge should also be included. Details on the management of the drainage system shall also be included. The approved scheme must be implemented prior to beneficial occupation.  This is to ensure that effective drainage facilities are provided for the proposed development and that flood risk is not increased elsewhere.

G. Thelwell-Davies

Engineer - Environment

for Operational Manager - Engineering

ar ran Rheolwr Gweithredol Priffyrdd a Pheirianneg