Vale of Glamorgan County Council

Dock Office

Holton Road

Barry Docks

Barry

CF63 4RT

|  | Date: 28/06/2019 |
| --- | --- |
|  | Our Ref: PLA0043019 |
|  | Your Ref: SAB.FUL.2019.001 |

# Dear Sir

Grid Ref: ST1054769185 310547 169185

Site: Whitmore High School, Port Road, West Barry, Vale of Glamorgan

Development: SAB Consultation - Existing school to be redeveloped to provide improved learning and sports facilities

We refer to your planning consultation relating to the above site, and we can provide the following comments in respect to the proposed development.

APPRAISAL

As statutory consultee, we welcome the opportunity to comment on this SAB application for surface water drainage proposals at Whitmore High School, Port Road West, Barry, in accordance with Schedule 3 of the Flood & Water Management Act 2010. Our comments are provided in response to the hierarchy (S1) and fixed standards (S2 – S6), as highlighted in the Welsh Government 'Statutory standards for sustainable drainage systems', and on the basis of information provided by the SAB application. Should the proposal alter during the course of the application process we kindly request that we are re-consulted and reserve the right to make new representation.

Standard S1 – Surface Water Runoff Destination

As a hierarchy standard, we acknowledge that S1 provides an assessment on the choice of runoff destination by way of 5 Levels with the most preferred level represented by Priority Level 1, and movement from Level 1 to lower levels determined by demonstration that the exception criteria apply. This standard highlights that discharges to sewerage systems must be limited where possible and that Priority Levels 4 and 5 should only be used in exceptional circumstances. Accordingly, we offer the following comments to each of the 5 Levels:

Priority Level 1: Collected for use

The submitted application form, and accompanying ‘Drainage Strategy’ (Ref: 26W006-ATK-0-X-RP-D-8100), indicates that the applicants have investigated use of rainwater harvesting to collect surface water flows and concluded that this runoff destination would be unviable. Having regard to the ‘Drainage Strategy’, we acknowledge that the cost effectiveness of such systems would preclude the use of rainwater harvesting and therefore accept that this runoff destination has been suitably investigated and discounted.

Priority Level 2: Infiltrated to Ground

The submitted application form, ‘Drainage Strategy’ (Ref: 26W006-ATK-0-X-RP-D-8100), and accompanying suite of plans, indicates proposals to discharge surface water flows into an infiltration basin via a variety of SuDS features. In principle we offer no objection subject to consultation with the Building Regulations Authority / Approved Building Inspector as the regulatory body.

Priority Level 3: Discharged to a Surface Water Body

The submitted application form, and accompanying ‘Drainage Strategy’ (Ref: 26W006-ATK-0-X-RP-D-8100), indicates that the applicants have investigated discharge into a surface water body and concluded that this runoff destination would be unviable. Having regard to the ‘Drainage Strategy’, we acknowledge that the distance to the nearest watercourse would preclude discharge to a surface water body and therefore accept that this runoff destination has been suitably investigated and discounted.

Priority Level 4: Discharged to a Surface Water Sewer, Highway Drain, or another Drainage System

The submitted application form, ‘Drainage Strategy’ (Ref: 26W006-ATK-0-X-RP-D-8100), and accompanying suite of plans, indicates some surface water flows will be moderated and remain discharging to the surface water sewer as an exceedance route from the on-site swales and infiltration basin. We acknowledge the proposals would provide a betterment of at least 40% and is only designed to utilise the surface water sewer, as an exceedance route, in very intense storm events. Notwithstanding this, we would advise that this appears to be a private sewer and in principle we offer no objection subject to consultation with the riparian owner of this drainage system.

Priority Level 5: Discharged to a Combined Sewer

We acknowledge that the application does not propose to discharge surface water flows into a combined sewer.

Standard S2 – Surface Water Runoff Hydraulic Control

We acknowledge that the aim of Standard S2 is to manage the surface water runoff from and on site in order to prevent any morphological damage and flooding risk, up to a suitable return period, in the interests of protecting public health.

As above, we offer no objection to proposals for disposal of surface water flows into an infiltration basin, with an exceedance route into a private surface water sewer subject to consultation and agreement with the Building Regulations Authority / Approved Building Inspector as the regulatory body as well as the riparian owner of the private sewerage system.

Standard S3 – Water Quality

We acknowledge that the aim of Standard S3 is to minimise the potential pollution risk posed by the surface water runoff to the receiving water body.

As above, we offer no objection to proposals for disposal of surface water flows into an infiltration basin, with an exceedance route into a private surface water sewer subject to consultation and agreement with the Building Regulations Authority / Approved Building Inspector as the regulatory body as well as the riparian owner of the private sewerage system.

Standard S4 – Amenity

We acknowledge that the aim of Standard S4 is to ensure that, where possible, the design of SuDS enhance the provision of high quality, attractive public space which contribute to health and wellbeing, liveability for local communities, and improving climate resilience.

As above, we offer no objection to proposals for disposal of surface water flows into an infiltration basin, with an exceedance route into a private surface water sewer subject to consultation and agreement with the Building Regulations Authority / Approved Building Inspector as the regulatory body as well as the riparian owner of the private sewerage system.

Standard S5 – Biodiversity

We acknowledge that the aim of Standard S5 is to ensure the design of SuDS create rich ecological corridors and enrich biodiversity value to is maximum potential.

As above, we offer no objection to proposals for disposal of surface water flows into an infiltration basin, with an exceedance route into a private surface water sewer subject to consultation and agreement with the Building Regulations Authority / Approved Building Inspector as the regulatory body as well as the riparian owner of the private sewerage system.

Standard S6 – Design

We acknowledge that the aim of Standard S6 is to ensure the design of surface water drainage systems are robust, can be easily and safely constructed, maintained and operated, to minimise impacts on the environment and natural resources.

As above, we offer no objection to proposals for disposal of surface water flows into an infiltration basin, with an exceedance route into a private surface water sewer subject to consultation and agreement with the Building Regulations Authority / Approved Building Inspector as the regulatory body as well as the riparian owner of the private sewerage system.

CONCLUSION

Having regard to our appraisal for each of the standards (S1 – S6), as highlighted in the Welsh Government 'Statutory standards for sustainable drainage systems', we offer no objection in principle to the SuDS proposals, on the basis of information provided by the SAB application. Accordingly, if you are minded to grant SAB Consent for this application, we would request that the following Condition and Advisory Notes are included within the consent to ensure no detriment to existing residents or the environment and to Dwr Cymru Welsh Water's assets:

Condition

No surface water and/or land drainage shall be allowed to connect directly or indirectly with the public sewerage network.

Reason: To prevent hydraulic overloading of the public sewerage system, to protect the health and safety of existing residents and ensure no pollution of or detriment to the environment

Advisory Notes

Please note that this SAB consent relates solely to the approval of SuDS components. In order to establish whether the proposed development benefits from consent, the applicant is advised to refer to the planning permission granted as well as any conditions in reference to foul water drainage. In accordance with the Town & Country Planning (Development Management Procedure)(Wales)(Amendment) Order 2016 Dwr Cymru Welsh Water is a statutory consultee to the planning process and will provide comments to any proposals for foul water drainage by response to a planning application consultation.

The applicant is also advised that some public sewers and lateral drains may not be recorded on our maps of public sewers because they were originally privately owned and were transferred into public ownership by nature of the Water Industry (Schemes for Adoption of Private Sewers) Regulations 2011. The presence of such assets may affect the proposal. In order to assist us in dealing with the proposal the applicant may contact Dwr Cymru Welsh Water. Under the Water Industry Act 1991 Dwr Cymru Welsh Water has rights of access to its apparatus at all times.

Our response is based on the information provided by your application.  Should the proposal alter during the course of the application process we kindly request that we are re-consulted and reserve the right to make new representation.

If you have any queries please contact the undersigned on 0800 917 2652 or via email at developer.services@dwrcymru.com

Please quote our reference number in all communications and correspondence.

# Yours faithfully,

Sion Jones

Development Control Officer

Developer Services