# Vale of Glamorgan

Highway Authority Observation Sheet

| Planning Application Ref: | 2019/00690/FUL |
| --- | --- |
| Observations By: | Tony Godsall |
| Date: | 29th October 2019 |
| Location: | The Spinney, Twyncyn, Dinas Powys |
| Proposal: | Proposed change of use from Granny annexe and studio, to a new home school class D1 |
| Case Officer: | Mr. S. D. Butler |

Detailed information has now been provided in respect of the Automatic Traffic Counter (ATC) Data including their location and from the data for ATC 1 there were on average approximately 145 vehicles per day utilising Twyncyn during weekdays and their 85%ile speed was 20mph. The data for ATC 2 indicated that there were on average approximately 83 Vehicles per day utilising Beauville Lane during weekdays and their 85%ile speed was 16mph.

As a result of the low vehicular speeds at ATC 2 then the Highway Authority considers that there would be no benefit in introducing Slow / Araf markings on the road and the cutting back of existing vegetation / trees as due to the current low speeds of vehicles this type of signage would unlikely reduce the speed of traffic further.

# Vale of Glamorgan

Highway Authority Observation Sheet

| Planning Application Ref: | 2019/00690/FUL |
| --- | --- |
| Observations By: | Tony Godsall |
| Date: | 22nd October 2019 |
| Location: | The Spinney, Twyncyn, Dinas Powys |
| Proposal: | Proposed change of use from Granny annexe and studio, to a new home school class D1 |
| Case Officer: | Mr. S. D. Butler |

Further to reviewing the above application as a result of the revised information that has been submitted the Highway Authority would comment as follows on the previous observations

1	From the information provided it was noted that an Automatic Traffic Counter was installed on Twyncyn which provided information on the number of vehicles utilising the road.  However, no information was provided in relation to the counters location or speed data associated with the vehicles utilising the road. As a result of the lack of detailed information provided the Highway Authority is still of the opinion that mitigation measures should be introduced on the lane to the West due to the partial visibility available by the introduction of Slow / Araf markings on the road and the cutting back of existing vegetation / trees.

2	The Technical Note contains a drawing of the proposed layout and swept path showing that a 3.5T vehicle can turn within the confines of the property and the Highway Authority is satisfied with that information

3	No information has been provided in respect of the width of the access serving the development, however as a result of the revised proposal that children will now be escorted on foot (walking bus) from the Bowls Club instead of utilising minibuses directly to the property and the ability of children to walk on the grass adjacent to the lane then there is now no requirement to widen the access.

4	No information has been provided in respect of the passing bays along the access road serving the development, however as a result of the revised proposal that children will now be escorted on foot (walking bus) from the Bowls Club instead of utilising minibuses directly to the property and the ability of children to walk on the grass adjacent to the lane then there is now no requirement to provide passing bays along the access road.

5	The spaces provided for staff and visitors are satisfactory

6	As a result of further information being provided on the location of the drop off point and the route the pupils would now take when being accompanied by a member of staff (walking bus) the Council’s Road Safety staff have undertaken a risk assessment of that route in accordance with the Learner Travel Statutory Provision and Operational Guidance June 2014. The risk assessment has highlighted that various actions and recommendations need to be undertaken by the school and is attached for information and action.

7	The Road from Twyncyn to the ‘Spinney’ is a private lane and as a result has not been included within the Learner Travel Statutory Provision and Operational Guidance Assessment. It is a matter for the School to undertake a risk assessment and to consider the Health and Safety requirements of that private lane

# Vale of Glamorgan

Highway Authority Observation Sheet

| Planning Application Ref: | 2019/00690/FUL |
| --- | --- |
| Observations By: | Tony Godsall |
| Date: | 12 August 2019 |
| Location: | The Spinney, Twyncyn, Dinas Powys |
| Proposal: | Proposed change of use from Granny annexe and studio, to a new home school class D1 |
| Case Officer: | Mr. S. D. Butler |

Further to a recent site inspection carried out in relation to the above application and considering the submitted drawings, the Highway Authority would comment as follows

- The highway is classed as a 30mph road and the normal requirement is for visibility splays of 2.4m x 43.0m in both directions along the adjacent highway from the means of access. Within the visibility envelope, no obstructions, inclusive of fencing and boundary walls are to exceed 600mm in height and any planting shall be located at the rear of the visibility splays. As can be seen from the photographs below, appropriate visibility is available to the west and south of the proposed access. However there is limited visibility to the West of the access. Due to the limited vehicular traffic to the West and no road casualties within the vicinity, mitigation measures could be introduced on the lane to the West due to the partial visibility available by the introduction of Slow / Araf markings on the road and the cutting back of existing vegetation / trees.

2	No drawing of the proposed parking and access arrangements within the property have been provided. For information, private drives over the length of 45m, need a turning head 4.8m by 14m to allow emergency vehicles and service deliveries to turn within the site curtilage and emerge onto the highway in a forward gear as stated in Manual for Streets paragraph 6.7.

3	The access serving the existing dwelling along the private access and the proposed development shall be provided at 4.5m for the first 10.0m from the adopted highway in order that two vehicles are able to pass side by side when entering/exiting the site in order to prevent vehicles queuing or reversing into the adjacent highway in the interest of highway safety.

No passing bays have been provided along the access road to the development and a plan is required indicating their position in order to prevent reversing vehicles which raises road safety issues for any pedestrians walking along the private access road.

4	It was noted in the Access Statement that the age range for the home school will be between 10 and 12 and limited to 10 children per class. In according to the Council’s Car Parking Standards for secondary schools, a requirement of 1 commercial vehicular space, 1 space per teacher (2No), 1 space per ancillary staff (No information has been provided), 3 visitor spaces and bus / mini bus parking as required (no information has been provided). The Highway Authority therefore requires the number of ancillary staff, type of commercial vehicles likely to be used and number of minibuses serving the school. It was noted from the site visit that the existing parking space availability would not allow the vehicles associated with the proposal to park and manoeuvre within the current constraints and as a result a 1/200 drawing of the proposed location and turning availability of these parking spaces area required.

5	The Access Statement indicated the following

“…..but the bigger site geography will be bringing the children from the agreed drop off point, as detailed on the transport document, while one of the teachers walk the children to the school, via the existing pavement networks.”

From the site visit it was noted that there is limited availability of footways along Twyncyn or along the joint private access road to the school. In order to ensure the safety of children then there will be a requirement to provide a footway along the verge and constructed to highway adoptable standard from the junction of Britway Road / Twyncyn Junction to the private access road. The Access statement also states that there will be an agreed drop off point and no location has been indicated.

Failure to provide the information required as a result of the comments above may result in an objection from the Highway Authority on road safety grounds