| To / I: | Mr William Groom |  | From / Oddi Wrth: | Operational Manager Environment and Engineering |
| --- | --- | --- | --- | --- |
| Dept / Adran: | Planning |  |  |  |
|  |  |  | My Ref / Cyf: | HE/SP/MN/L5/1 |
| Date / Dyddiad: | 15/04/2024 |  | Tel / Ffôn: | 02920 673 075 |
| Your Ref / Eich Cyf: | P/DC/LC/WG/2024/00224/FUL |  | Fax / Ffacs: | 02920 673 114 |

Subject / Testyn:	Planning Application No. 2024/00224/FUL (WG), Bolston House, Bonvilston

Proposal:	Demolition of the existing dwelling and re-development of the site to accommodate residential development and associated works

This site is located within DAM Zone A which is not considered to be at risk to fluvial and coastal / tidal flooding. NRW flood maps (TAN15 2004) indicate that this site is at a very low risk of surface water flooding.

A drainage statement has been provided indicating the intent to discharge surface water into a combined sewer.

This application is subject to SAB approval prior to any commencement of work. As such a detailed design for the surface water drainage will be required to be submitted through the SAB process.

Advisory:

New developments of more than one dwelling or where the area covered by construction work equals or exceeds 100 square metres as defined by The Flood and Water Management Act 2010 (Schedule 3), will require SuDS Approval Body (SAB) approval prior to the commencement of construction.

Further information of the SAB process can be found at our website or by contacting our SAB team: sab@valeofglamorgan.gov.uk

Yours Sincerely

Matthew Nicole

Assistant Engineer – Environment

for Operational Manager Highways and Engineering

ar ran Rheolwr Gweithredol Priffyrdd a Pheirianneg