| To / I: | Yvonne Pritchard |  | From / Oddi Wrth: | Operational Manager Highways and Engineering |
| --- | --- | --- | --- | --- |
| Dept / Adran: | Planning |  |  |  |
|  |  |  | My Ref / Cyf: | HE/SP/GTD/L5/1 |
| Date / Dyddiad: | 07/01/2019 |  | Tel / Ffôn: | 029 20673235 |
| Your Ref / Eich: Cyf: | P/DC/LC/YP/2018/01408/FUL |  | Fax / Ffacs: | 029 20673114 |

Subject / Testyn:	Planning Application No. 2018/01408/FUL Former Cowbridge Comprehensive School, Aberthin Road, Cowbridge

Proposal:	Proposed demolition of existing school, development of 48 dwellings (43 flats and five houses) and associated works

This site is not located in DAM zones at risk of tidal or fluvial flooding and NRW maps indicate that there is a very low risk of surface water flooding to the site.

The submitted drainage strategy indicates that infiltration testing will be undertaken to confirm if soakaways are a viable option, however no infiltration data has been provided with this application. For all new developments, infiltration should be the primary method of surface water disposal, prior to any other method being considered and evidence of on-site infiltration testing should be submitted prior to approval of a surface water drainage system. Therefore, prior to work commencing on site, a full drainage plan demonstrating how roof and yard water will be disposed of shall be submitted to and approved by the LPA. Should infiltration techniques be used, evidence of on-site porosity testing shall also be provided together with the standard of service the system shall provide. The surface water drainage scheme shall be designed so that flooding does not occur on any part of the site for a 1 in 30 year rainfall event plus climate change and not in any part of any building for a 1 in 100 year rainfall event plus climate change.

No details on the management and maintenance of the proposed drainage system have been included with this application. A management plan which includes details on future management responsibilities for the site and its drainage assets should be submitted and approved in writing by the LPA. This plan shall detail the strategy that will be followed to facilitate the optimal functionality and performance of the SuDS scheme throughout its lifetime.

Conditions:

Given the above, no development shall commence on site until a detailed scheme for the surface water drainage of the site, showing how road and roof / yard water will be dealt with has been submitted and approved in writing by the LPA. If infiltration techniques are used, then the plan shall include the details of field percolation tests. Any calculations for onsite attenuation or discharge should also be included together with the details on the management of the drainage system. The approved scheme must be implemented prior to beneficial occupancy. This is to ensure that effective drainage facilities are provided for the proposed development and that flood risk is not increased elsewhere.

Gareth Thelwell-Davies

Engineer – Environment

for Operational Manager Highways and Engineering

ar ran Rheolwr Gweithredol Priffyrdd a Pheirianneg