Arboricultural Impact Assessment

for

Bolston House,

Bonvilston.

Inspected by:-

Julian Wilkes BSc.For, MSc.Land Man, MIC.For, TechArb

Treescene Ltd

The Walled Garden

Old Coedarhydyglyn

St Nicholas

Cardiff

CF5 6SG

Tel No. 029 20599300

22nd November, 2021

Registered Office:  Treescene Limited

The Walled Garden, Old Coedarhydyglyn, St. Nicholas, Cardiff CF5 6SG

Tel. 029 205 99300 Email. trees@treescene.co.uk

- BRIEF

I have been instructed by Transworld Real Estate Ltd to prepare an Arboricultural Impact Assessment (AIA) in relation to a proposed development at Bolston House, Bonvilston.

- TREE SURVEY AND PLAN

The information within this document is based on the Treescene Tree Survey dated 13.08.20, the Treescene AIA Plan 11/2021 and the Treescene Tree Retention/Removal Plan 11/2021.

- TREES TO BE REMOVED

a. Arboricultural Reasons

Trees T8, T10, T11, T14, G15, G17, T19, T20, T21, T22, G23, G26, T28, T30, T38, T39, T41, T42, T45, T46, G47, T48, T51, T55, T59, T60, G61 and T63 are recommended for removal in the Tree Survey due to poor quality (U category).

b. To Facilitate Development

Trees T1, G2, G3, G4, G5, G6, G7, G9, T12, G13, T16, G18, G24, T25, T27, T29, T31, T32, G44 and T49 are proposed for removal to accommodate the development layout.

These are all C category trees (low quality) except T12, T27 and T31 (B category, moderate quality).

Trees to be removed are indicated on the attached Treescene Tree Retention/Removal Plan 11/2021.

- TREE PRUNING

Many of the trees to be retained contain structural defects/deadwood or may impede vehicle/pedestrian movements within the site. Works to improve tree safety or remove a potential source of nuisance are detailed in the Preliminary Management Recommendations within the Tree Survey. All pruning and felling/coppicing works are to be undertaken by suitably qualified and experienced Arboricultural Contractors working to BS3998:2010 Recommendations for Tree Work.

Some additional crown raising work to specific trees may be required once the final planning layout is agreed. These additional pruning works should be detailed in a site specific Arboricultural Method Statement (AMS).

- ROOT PROTECTION AREA (RPA) INCURSIONS

There are no conflicts between proposed structures and RPAs of trees to be retained apart from in the following circumstances;

T50 - corner of garage to the south east,

T54 - car parking and drive to the east,

T65 - drive to the east,

T68 - drive to the east.

In all circumstances the incursions are slight (mainly less than 5% of the total RPA affected, all less than 10%) and therefore there will be minimal adverse impact upon the future health of the affected trees. However, in order to ensure that the affected trees are not damaged as a result of the development special excavation and construction techniques, to be detailed in a site specific Arboricultural Method Statement (AMS), will be employed in these areas.

- PROTECTION OF RETAINED TREES

All trees to be retained should be protected by fencing in accordance with the details in BS5837:2012. The implementation of the tree protection on site should be in compliance with a site specific Tree Protection Plan (TPP) and AMS. A draft Treescene TPP 11/2021 indicating proposed positions of protective barriers and areas of no-dig construction is attached.

- IMPACT ON LOCAL AMENITY

Tree loss in relation to the development focuses primarily in the clearance of low quality trees in the interior of the site, mainly to create the site access and internal roads as well as to create space to install plots in the southern section of the site. The existing robust tree belts on boundaries of the northern section of the site are retained thus minimising any wider landscape impacts.

Extensive new tree planting within the site is proposed thus mitigating any tree loss and contributing to an enhancement of the local tree stock as a result of the proposed development.