Vale of Glamorgan County Council

Dock Office

Holton Road Barry Docks

Barry

CF63 4RT

|  | Date: 30/09/2022 |
| --- | --- |
|  | Our Ref: PLA0068007 |
|  | Your Ref: 2022/00958/FUL |

# Dear Sir/Madam

Grid Ref: SS994739 299626 173992

Site: Land between Windmill Lane and St Athan Road, Cowbridge

Development: Residential development of up to 105 dwellings, open space and associated highway and drainage infrastructure

We refer to your planning consultation relating to the above site, and we can provide the following comments in respect to the proposed development.

SEWERAGE

We note from the applicants “drainage strategy”, the proposal to dispose of foul water from the development is to connect into the existing foul sewer located on Windmill Lane. Also noting the proposal for the disposal of surface water is through the use of a sustainable drainage system. We offer no objection to the proposal.

We can confirm capacity exists within the public sewerage network in order to receive the domestic foul only flows from the proposed development site.

As of 7th January 2019, this proposed development is subject to Schedule 3 of the Flood and Water Management Act 2010. The development therefore requires approval of Sustainable Drainage Systems (SuDS) features, in accordance with the 'Statutory standards for sustainable drainage systems – designing, constructing, operating and maintaining surface water drainage systems'. It is therefore recommended that the developer engage in consultation with the Local Authority, as the determining SuDS Approval Body (SAB), in relation to their proposals for SuDS features. Please note, Dwr Cymru Welsh Water is a statutory consultee to the SAB application process and will provide comments to any SuDS proposals by response to SAB consultation.

Turning to potable water we advise that the proposed development is in an area where there are water supply problems. We had the opportunity to comment at pre-planning and advised that a hydraulic modelling assessment was required to identify a potential point of connection.

Therefore, if you are minded to grant planning permission we request that the following condition and Advisory Notes are included within any subsequent consent.

Condition

No development shall take place until a point of connection on the potable water system has been identified by a hydraulic modelling assessment, which shall be first submitted to and approved by the local planning authority. Thereafter the connection shall be made in accordance with the recommended connection option following the implementation of any necessary improvements to the potable water system, as may be identified by the hydraulic modelling assessment.

Reason: To ensure the site is served by a suitable potable water supply.

No surface water and/or land drainage shall be allowed to connect directly or indirectly with the public sewerage network

Reason: To prevent hydraulic overloading of the public sewerage system, to protect the health and safety of existing residents and ensure no pollution of or detriment to the environment

Advisory Notes

In accordance with Planning Policy Wales (Edition 11) and Technical Advice Note 12 (Design), the applicant is advised to take a sustainable approach in considering water supply in new development proposals, including utilising approaches that improve water efficiency and reduce water consumption. We would recommend that the applicant liaises with the relevant Local Authority Building Control department to discuss their water efficiency requirements.

The applicant may need to apply to Dwr Cymru / Welsh Water for any connection to the public sewer under S106 of the Water industry Act 1991. If the connection to the public sewer network is either via a lateral drain (i.e. a drain which extends beyond the connecting property boundary) or via a new sewer (i.e. serves more than one property), it is now a mandatory requirement to first enter into a Section 104 Adoption Agreement (Water Industry Act 1991). The design of the sewers and lateral drains must also conform to the Welsh Ministers Standards for Gravity Foul Sewers and Lateral Drains, and conform with the publication "Sewers for Adoption"- 7th Edition. Further information can be obtained via the Developer Services pages of www.dwrcymru.com

The applicant is also advised that some public sewers and lateral drains may not be recorded on our maps of public sewers because they were originally privately owned and were transferred into public ownership by nature of the Water Industry (Schemes for Adoption of Private Sewers) Regulations 2011.  The presence of such assets may affect the proposal.  In order to assist us in dealing with the proposal the applicant may contact Dwr Cymru Welsh Water on 0800 085 3968 to establish the location and status of the apparatus. Under the Water Industry Act 1991 Dwr Cymru Welsh Water has rights of access to its apparatus at all times.

Our response is based on the information provided by your application.  Should the proposal alter during the course of the application process we kindly request that we are re-consulted and reserve the right to make new representation.

If you have any queries please contact the undersigned on 0800 917 2652 or via email at developer.services@dwrcymru.com

Please quote our reference number in all communications and correspondence.

# Yours faithfully,

# Chris Scourfield

# Development Planning Officer

# Developer Services